## Slide 1: FPGA Bitstream Security: A Day in the Life
1Adam Duncan, 2Fahim Rahman, 1Andrew Lukefahr, 2Farimah Faramandi, 2Mark Tehranipoor
adamdunc@iu.edu
1Indiana University
2University of Florida

## Slide 2: Outline
FPGA Background
Five Bitstream Stages
  Attacks
  Countermeasures
Future FPGA Bitstream Security
Conclusion

## Slide 3: FPGA: Field Programmable Gate Array
Map
FPGAs implement custom digital hardware

## Slide 4: FPGA Usage is Growing…
Benefits:
Reconfigurable
Short development times
Low NRE costs
Simplified design flows
Close to ASIC performance
Figure: Adapted from Trimberger2014 “Three ages of FPGAs”
ASIC
FPGA
28 nm
16 nm
Number of Units
NRE
Total Cost
Xilinx FY19 revenue = $3.09B

## Slide 5: Historical FPGA Design Flow
User
Design
Bitstream
FPGA
Manufacturer
Bitstream Development Software
FPGA

## Slide 6: Current FPGA Design Flow
Bitstream
FPGA
Manufacturer
Bitstream Development Software
FPGA
System Integrator
System Programmer
System In-Field
Recycler
(E-Waste)
3PIP Design
House
In-House IP

## Slide 7: Bitstream Stages
System Integrator
System Programmer
System In-Field
Bitstream-Generation
Bitstream-at-Rest
Bitstream- Running
Bitstream-Loading
Bitstream-EOL and Counterfeiting
Recycler
(E-Waste)
3PIP Design
House
Entities
Stages
In-House IP
We define five bitstream stages

## Slide 8: Bitstream Stages Interaction
System Integrator
System Programmer
System In-Field
Bitstream-Generation
Bitstream-at-Rest
Bitstream- Running
Bitstream-Loading
Bitstream-EOL and Counterfeiting
Recycler
(E-Waste)
3PIP Design
House
Design Changes
Design Checkpoints
Bitstream in NVM
Bitstream to NVM
Bitstream Compiled
PCB Extraction
System Operating
Booting from NVM
Remote
Upgrade
Design Changes
System Decommissioned
Functional Test
Entities
Stages
In-House IP
Complicated interactions…
Let’s focus on bitstream stages

## Slide 9: Bitstream Stages + Threats
System Integrator
System Programmer
System In-Field
Bitstream-Generation
Bitstream-at-Rest
Bitstream- Running
Bitstream-Loading
Bitstream-EOL and Counterfeiting
Recycler
(E-Waste)
3PIP Design
House
Design Changes
Design Checkpoints
Bitstream in NVM
Bitstream to NVM
Bitstream Compiled
PCB Extraction
System Operating
Booting from NVM
Remote
Upgrade
Design Changes
System Decommissioned
Malicious Intent
Non-Malicious
Intent
Functional Test
Entities
Stages
Threats
Bitstream Tampering
IP
Piracy
Side Channel Attacks
Replay
Attacks
Fault Injection
Run-time Attacks
Bitstream
Remanence
Counterfeit
FPGAs
In-House IP

## Slide 10: Bitstream-Generation
System Integrator
System Programmer
System In-Field
Bitstream-Generation
Recycler
(E-Waste)
3PIP Design
House
Design Changes
Design Checkpoints
Design Changes
Malicious Intent
Non-Malicious
Intent
Entities
Stages
Threats
In-House IP

## Slide 11: Bitstream-Generation: Flow
Trojan Insertion
IP Piracy
Lookup Tables vs. Standard Cells
Switch Matrices
FPGA-specific threats from synthesis onward

## Slide 12: Bitstream-Generation: Attacks
Figure: Krieg2016 “Malicious lut: a stealthy fpga trojan injected and triggered by the design flow”
FPGA fabric fixed, but configurable…
Multiple Trojan insertion points
Attack goals:
  Modify logic/interconnects
  Leak information
  Target unused resources
Attack vectors:
  Malicious HDL
  EDA tool usage
    Malicious (Trojan)
    Non-malicious (HLS - Leaky Crypto)

## Slide 13: Bitstream-Generation: Countermeasures
Figure: Zhang2015 “A puf-fsm binding scheme forfpga ip protection and pay-per-device licensing”
IP functionality tied to FPGA silicon properties (PUF)
EDA tool level:
  Best software practices
RTL level:
  Trojan detection (rare nodes)
  IP encryption (IEEE p1735)
Logic block level:
  RTL Logic locking
  Fill unused area and test (BISA)
  Physically unclonable functions (PUFs)

## Slide 14: Bitstream-at-Rest
System Integrator
System Programmer
System In-Field
Bitstream-at-Rest
Recycler
(E-Waste)
3PIP Design
House
Design Changes
Design Checkpoints
Bitstream in NVM
Bitstream to NVM
Bitstream Compiled
Design Changes
Functional Test
Entities
Stages
Threats
Bitstream Tampering
IP
Piracy
In-House IP

## Slide 15: Bitstream-at-Rest: Attacks
Vendor bitstream protections:
  Encryption/Authentication
  Vendor-proprietary formatting
Figure: Zhang2019 “A comprehensive fpga reverse engineering tool-chain: From bitstream to rtl code”
Bitstream attacks:
  Tamper bitstream
    Add malicious content
    Bypass licensing
  Extract IP from bitstream
    Steal IP
    Overproduction
Bitstream to netlist

## Slide 16: Bitstream-at-Rest: Countermeasures
Figure: Peterson2018, “Xapp1323: Developing tamper-resistant designs with zynq ultrascale+ devices”
Red key decrypts.
Black key stored in FPGA.
Vendor hardware level:
  Encryption
  Authentication
  On-chip bitstream storage
RTL level:
  Watermarks
Logic block level:
  Bitstream-level logic locking

## Slide 17: Bitstream-Loading
System Integrator
System Programmer
System In-Field
Bitstream-Loading
Recycler
(E-Waste)
3PIP Design
House
Booting from NVM
Functional Test
Entities
Stages
Threats
Side Channel Attacks
Replay
Attacks
In-House IP

## Slide 18: Bitstream-Loading: FPGA Memory Types
“Store in Memory IC”
Bitstream
Memory IC
FPGA
Flash: 0.5M Logic Gates​, 28 nm
Antifuse: 2M Logic Gates, 150 nm
“Store in FPGA”
FPGA
Bitstream
SRAM: 90M Logic Gates, 16 nm
~90% FPGA market share
Best Bitstream Security
Best Performance
What about emerging non-volatile memories?

## Slide 19: Bitstream-Loading: Attacks
Side channel attacks:
  Power, timing, imaging
  Information Leakage
Figure: Zhang2015 “Reconfigurable Binding against FPGA Replay Attacks”
Replay attacks:
  Load old bitstream to expose vulnerability
Replay attack loads older vulnerable bitstream

## Slide 20: Bitstream-Loading: Countermeasures
Figure: Peterson2018, “Xapp1323: Developing tamper-resistant designs with zynq ultrascale+ devices”
Encrypted FSBL Authentication
Vendor hardware level:
  Encrypted FSBL
  Side channel defenses
Vendor software level:
  Bitstream versioning
User level:
  Custom FSBL
Encrypted FSBL Authentication

## Slide 21: Bitstream-Running
System Integrator
System Programmer
System In-Field
Bitstream- Running
Recycler
(E-Waste)
3PIP Design
House
System Operating
Remote
Upgrade
Entities
Fault Injection
Run-time Attacks
In-House IP
Stages
Threats

## Slide 22: Bitstream-Running: Attacks
Fault injection:
  Glitches (power, clock, EM, laser, temperature)
  Bit errors (ionizing radiation)
Run-time threats:
  Partial reconfiguration
  Shared tenancy
AWS shared tenancy
Shared power distribution network (PDN) attack
Figure: Trimberger2017, “Security of FPGAs in Data Centers”
Figure: Schellenberg2018, “An inside job: Remote power analysis attacks on fpgas”

## Slide 23: Bitstream-Running: Countermeasures
Figure: Xilinx2015, “Security monitor ip core product brief”
Xilinx Secmon Tamper detection IP core
Vendor hardware level:
  Sensors (temperature, voltage, …)
  Side channel defenses
  Configuration memory hashing
Vendor software level:
  Bitstream screening
  Vulnerable node identification
User level:
  Tamper-resistant designs
  Partial reconfiguration hashing
  Tamper detection IP cores

## Slide 24: Bitstream-EOL
System Integrator
System Programmer
System In-Field
Bitstream-EOL and Counterfeiting
Recycler
(E-Waste)
3PIP Design
House
PCB Extraction
System Decommissioned
Entities
Stages
Threats
Bitstream
Remanence
Counterfeit
FPGAs
In-House IP

## Slide 25: Bitstream-EOL: Attacks
Bitstream remanence:
  Bitstream still on board NVM
  Bitstream still on Flash/antifuse FPGA
FPGA counterfeits:
  Harvested from e-waste
  Remarked legacy devices
FPGAs = 20% of counterfeits
Figure: Akhoundov2018, “2017 erai reported parts analysis”

## Slide 26: Bitstream-EOL: Countermeasures
Figure: Microsemi2018, “Polarfire FPGA security user guide”
Microsemi zeroization options
Vendor hardware level:
  Bitstream zeroization
  Key zeroization
  Supply chain tracking keys
Vendor software level:
  Supply chain tracking
  Segmented locking
User level:
  Partial reconfiguration for zeroization
  Aging detection

## Slide 27: Future FPGA Bitstream Security
FPGA memory technologies:
  Currently: SRAM/Flash/antifuse
  Trending: Nonvolatile MRAM/ReRAM
  Impact: Improved bitstream storage security? New physical attacks?
Advanced FPGA packaging:
  Currently: FPGA and FPGA SoCs
  Trending: Tiling, MCP
  Impact: Reduced physical attack surface? Untrusted ICs in package?

## Slide 28: Future FPGA Bitstream Security
FPGA bitstream initialization and upgrade:
  Currently: ISP physically connected to FPGA
  Trending: Remotely loading, updating and authenticating bitstreams
  Impact: Improved programming times? New bitstream tampering attacks?
Multi-FPGA systems and shared tenancy:
  Currently: Single FPGA or SoC FPGA per system
  Trending: Multiple FPGAs in system, multiple users sharing FPGA resources
  Impact: Improved system time-to-market? Shared FPGA resource attacks?

## Slide 29: Conclusion
Bitstream Stages:
  Bitstream-Generation
  Bitstream-at-Rest
  Bitstream-Loading
  Bitstream-Running
  Bitstream-EOL
Robust FPGA security should consider protection across all stages