## Slide 1
FLATS: Filling Logic and Testing Spatially for FPGA Tamper Detection and Authentication
Adam Duncan1,2, Grant Skipper1,2, Andrew Stern3, Adib Nahiyan3, Fahim Rahman3,
Andrew Lukefahr2, Mark Tehranipoor3, Martin Swany2
NSWC Crane1
Indiana University2
University of Florida3

## Slide 2: Problem: Post-Synthesis Threats
Generate Bitstream
Program FPGA
In Field
IP
Synthesis
Place and Route
FPGA Lifecyle
Configuration Tamper Locations
Configuration Tampering: Modifying bitstream to change design functionality
Configuration Tampering Motivations: Malicious insertion (Hardware Trojan)
Profit (IP Piracy)

## Slide 3: FPGA Configuration Tamper Security
Defenses:
Bitstream encryption – Key extraction
Xilinx FPGA | Introduced | Vulnerability
Virtex II | 2001 | [MBKP11]
Virtex 4 | 2005 | [MKP12]
Virtex 5 | 2006 | [MKP12]
6 series | 2009 | [MS16]
7 series | 2010 | [MS16]
UltraSCALE | 2014 | [LTKBS18]
Research community continues to publish FPGA encryption key extraction papers

## Slide 4: FPGA Configuration Tamper Security
Defenses:
Bitstream encryption – Key extraction
Proprietary bitstream format - RE
Year | Author | Tool Name | Notable Feature
1999 | Guiccione |  | First known work
2002 | Raghavan | PARBITS | 
2002 | Horta | JPG | 
2006 | Ziener |  | Virtex II support
2008 | Note |  | Virtex 4/5 support
2010 | Lavin | Rapidsmith | 
2011 | Steiner | Torc | 
2012 | Benz | Bil | 
2013 | Ding |  | 
2017 | Pham | Bitman | API for 7-series+
2019 | Ender |  | RE + Trojan
Research community continues to publish bitstream reverse engineering papers

## Slide 5: FPGA Configuration Tamper Security
Defenses:
Bitstream encryption – Key extraction
Proprietary bitstream format - RE
CRC – Disable
Runtime bitflip scrubbing – Disable
We need additional FPGA configuration tamper detection techniques!
Detection:
JTAG verify – Spoofable
Runtime hashing – Bypass

## Slide 6: Our Idea: Out-of-Band Spatial Watermarking
Integrate oscillators into a design to generate energy at design-specific spatial locations
Use infrared (IR) imaging to confirm spatial locations and detect bitstream tampering
IP
IP
IP

## Slide 7: FLATS: Filling Logic and Testing Spatially
Generate Bitstream
Program FPGA
In Field
IP
Synthesis
Place and Route
Make Room for Partial Oscillators
FLATS Insertion
Fill Unused Logic
Integrate Partial Oscillators in Design
Add Logic Controller
Stimulate Logic Controller
Detect Spatially with IR
Activate Partial Oscillators
Compare with Expected
FLATS Verification
Authentic?
Y/N
Tamper Detected?
Y/N
FLATS inserted to perform out-of-band authentication and tamper detection

## Slide 8: FLATS Insertion Implementation
LFSR + Logic
Seed
ECID
User Input
ICAP
I1
I2
I3
I4
O1
O2
LUTA: O1 = 0
O2= I2 & I3 & I4
A
B
C
I1
I2
I3
I4
O1
O2
LUTB: O1 = 0
O2 = I2 ^ I3
D
Z
Z = (A & B & C) ^ D
After FLATS
‘1’
I1
I2
I3
I4
O1
O2
LUTA: O1 = open
O2 = I2 & I3 & I4
A
B
C
I1
I2
I3
I4
O1
O2
LUTB: O1 = open
O2 = I2 ^ I3
D
Z
Z = (A & B & C) ^ D
Original Post-Synthesis
Sequence

## Slide 9: FLATS Insertion Implementation
LFSR + Logic
Seed
ECID
User Input
ICAP
Seq N = 0x104008
LUT = 0x1 (LUT A)
LUT Init = 0x0400
Freq Div = 0x8
I1
I2
I3
I4
O1
O2
LUTA: O1 = !I1 & I2 & I3 & I4
O2= I2 & I3 & I4
A
B
C
I1
I2
I3
I4
O1
O2
LUTB: O1 = 0
O2 = I2 ^ I3
D
Z
Z = (A & B & C) ^ D
After FLATS
‘1’
0xA32F
0x92CD
I1
I2
I3
I4
O1
O2
LUTA: O1 = open
O2 = I2 & I3 & I4
A
B
C
I1
I2
I3
I4
O1
O2
LUTB: O1 = open
O2 = I2 ^ I3
D
Z
Z = (A & B & C) ^ D
Original Post-Synthesis
Sequence

## Slide 10: FLATS Insertion Implementation
LFSR + Logic
Seed
ECID
User Input
ICAP
Seq N = 0x204008
LUT = 0x2 (LUT B)
LUT Init = 0x0400
Freq Div = 0x8
I1
I2
I3
I4
O1
O2
LUTA: O1 = 0
O2= I2 & I3 & I4
A
B
C
I1
I2
I3
I4
O1
O2
LUTB: O1 = !I1 & I2 & I3 & I4
O2 = I2 ^ I3
D
Z
Z = (A & B & C) ^ D
After FLATS
‘1’
0xA32F
0x1D4F
I1
I2
I3
I4
O1
O2
LUTA: O1 = open
O2 = I2 & I3 & I4
A
B
C
I1
I2
I3
I4
O1
O2
LUTB: O1 = open
O2 = I2 ^ I3
D
Z
Z = (A & B & C) ^ D
Original Post-Synthesis
Sequence

## Slide 11: FLATS Verification Implementation
FPGA Die
FPGA Package
P&R
IR Lock-In
Beacons and Authenticators
4 Beacons
4 Authenticators
FPGA Design SW
IR Single Frame
IR after Lock-In
FLATS Insertion
FLATS Verification

## Slide 12: FLATS Authentication Example
Beacons and Authenticators
ISCAS-85 c432 Experimental Results
ISCAS-85 Benchmark Circuits
< 12% area penalty
~ 15 µW per oscillator
Tampered
Authenticator

## Slide 13: FLATS Resolution with COTS IR Imager
IR Lock-In
Beacons and Authenticators
Single-LUT tamper detection possible using 25 µm x 25 µm COTS IR imager
Prototype Setup
75 µm x 75 µm FPGA P&R
slice1
slice2
slice3
slice4
slice5
slice6
slice7
slice8
mirroring
IR Imaging
FPGA
75 µm
75 µm

## Slide 14: FLATS Deployable Run-Time Extension
FPGA Si Substrate
PCB
1Hz dT = 0.1C locations

## Slide 15: FLATS Deployable Run-Time Extension
FPGA Si Substrate
Substrate (Glass, Si, Flex material?)
Read Out IC
PCB
1Hz, 0.1C
Ethernet MAC
X,Y (SPI)
Challenge
Response

## Slide 16: Conclusion
FPGA configuration tampering is an emerging threat to FPGA security
FLATS integrates oscillators into a user design for out-of-band spatial detection
FLATS detects configuration tampering and performs authentication

## Slide 17: Backup

## Slide 18: FPGA Reconfigurability vs. Security
FPGA: Field Programmable Gate Array
Benefits:
Reconfigurable
Short development times
Low NRE costs
Simplified design flows
Close to ASIC performance
Figure: IDA report, Examination of DoD’s Use of Microelectronics in Weapon Systems, 2013